## Slide 1: Planning the project
What are the core functions to be provided by the project?
  Processing, power switching, data acquisition, communications, etc.
What ancillary functions are required to support the core functions?
  Power conversion and conditioning, timing, off-board connections, etc.
What EMC issues are predictable?
  Noisy switching power supplies, noise from MCUs and clocks, RF from transmitters
What are the budget constraints?
  Are there off-the-shelf solutions that are more cost-effective?

## Slide 2: Component selection
Flight heritage is valuable but should be balanced by actual conditions and requirements.
  A HAB mission, for example, is short-duration, so components are less likely to fail even under harsh conditions.
Choose common, mainstream components when possible.
  Widely-used components will have extensive resources and examples available.
  Availability is likely to be much better and costs lower.
Start with the most complex components (MCU/MPU, FPGA, etc.) and work outward from there.
  Most of the components on the board will be support for these complex ICs.

## Slide 3: Schematic entry
Most complex components will have manufacturer-developed reference implementations.
  These are schematics and PCB layouts designed to maximize the chance of a final project that works well.
  Take advantage of the reference implementation unless you have a very good reason to diverge.
Most integrated circuit datasheets will include example circuits. Example PCB layouts will be included for components with special requirements (switching power converters, for example).

## Slide 4: PCB layout
For cubesats, start with standard cubesat PCB template
Choose number of copper layers in the PCB
  Four layers should be considered standard, as it provides lots of trace routing flexibility and large areas of copper for shielding and thermal management.
  Two layers can be used for very simple PCBs.